# Industrial Monitor Converter

# (CGA/EGA/MDA/RGB to VGA)

# Model: HC1011

Hmwtech Co.,Ltd

Apr 2010

# .  Features

Hmwtech Co. , Ltd (H.M.W.) in the industrial equipment under long-term maintenance and reconstruction of the monitors& display systems on the lessons learned to gather requirements and feedback of many customers, after many years of development and testing, based on the strength in launch of innovative industrial monitor converter – HC1011, it achieved Industrial video signal(RGB/CGA/VGA  to VGA) conversion fully automated operation, will give you the maintenance and replacement of industrial display to bring about affordable price and convenient.

- Feature specifications

| Input | Signals | MDA、CGA、EGA、RGB、RGB Sog、RGBS、RGBHV、YPbPr |
| --- | --- | --- |
|  | Interface | 9pin、3pin、6pin、14pin、20pin、25pin |
|  | Horizontal Frequency Rate(H) | 12kHz to 40kHz automatically recognized |
| Output | Supports | 15pin VGA，Resolution:800*600/60HZ or custom-resolution |
|  | Interface | D-Sub 15 PIN standard VGA port |
| Power | DC 12V 1.0A |

Note:

1.YPbPr = YUV

2.Input Horizontal Frequency Rate 12kHz to 40kHz automatically recognized.

3.Support RGB and YPbPr

4.Support Interlaced Scanning and Line by Line Scanning.

5.Support Vertical Resolution from line200 to line 600 automatically recognized.

6.Support variable Horizontal Resolution automatically recognized。

7.Support RGBHV (separate sync) ,RGBS (composite sync), automatically recognized

8.Output resolution: 800*600/60Hz standard VGA or custom-resolution.

# 3.  Interface Specification

| Item | Spec. | Remarks |
| --- | --- | --- |
| ① V | To connect V interface of the input device | Input Channel Ⅰ |
| ② H/CS | To connect H(CS) interface of the input device |  |
| ③ R/Pr | Red signal input/ Pr signal input |  |
| ④ G/Y | Green signal input/ YPBPR -Y signal input |  |
| ⑤ B/Pb | Blue Signal input/YPBPR -Pb signal input |  |
| ⑥ RUN | Running Status Indicator |  |
| ⑦ VIDEO in | To connect 9-pin interface of the input device | Input Channel Ⅱ |
| ⑧ VGA out | Standard sub-15p VGA female interface | VGA Output |
| ⑨ MENU | Use to adjust screen /programming |  |
| ⑩ DC12 | Power input DC12V, 1A |  |

Note: Input Channel Ⅰ, Input Channel Ⅱ, you can choose one of them

4. Definition for I/O interface

Table 4.1 Definition for Input Channel Ⅱ:

| PIN | Input Signal |
| --- | --- |
| p1(GND) | Connect to the ground |
| p2(GND) | Connect to the ground |
| P3(R) | connect R(ed) interface of the input device |
| P4(G) | connect G(reen) interface of the input device |
| P5(B) | connect B(lue) interface of the input device |
| P6 | Undefined(null) |
| P7 | Undefined(null) |
| P8(H) | connect H(CS) interface of the input device |
| P9(V) | connect V interface of the input device |

Figure 4.1 Definition for Input Channel Ⅱ

Table 4.2 Definition for Input Channel Ⅰ

| BNC | Input Signal | Connection image |
| --- | --- | --- |
| Pb、Y、Pr | YPbPr input signal (right image) Interface: three BNC slot, connected to the corresponding Pb, Y, Pr interface, then Y monochrome port. | Figure 4.2 Analog 3BNC (YPBPR) Input. |
| R、G、B | RGB Sog input signal (right image) Interface: three BNC slot, connected to the corresponding R, G, B slot, then G monochrome port. | Figure 4.3 Analog 3BNC (RGB Sog) Input. |
| R、G、B、S | RGBS CS Composite Sync (right image) Interfaces: 4 BNC slot, connected to the corresponding R, G, B, S I, monochrome then G, S I | Figure 4.4 Analog 4BNC (RGBS CS) Input. |
| R、G、B、H、V | RGBHV separate sync (right image) Interface: 5 BNC port, connected to the corresponding R, G, B, H, V I, monochrome then G, H, V I | Figure 4.5 Analog 5BNC (RGBHV) Input. |

5. Operation Menu

6. Accessories& Details

Table 6.1 Accessories list

| Item | QTY | Remarks |
| --- | --- | --- |
| User’s Manual | 1 | English |
| Power Adaptor | 1 | DC12V,1A |
| half 9pin cable | 1 |  |
| 9pin M-F cable | 2 | 1 Male + 1 Female |

Table 6.2 Details of half 9Pin connector

| Name | Wire color | Signal |
| --- | --- | --- |
| A | Silver web | Shield |
| B | Black wire | Ground(GND) |
| C | White wire | Vertical Frequency Rate(V) |
| D | Orange wire | Horizontal Frequency Rate(H) |
| E | Blue wire | Blue(B) |
| F | Green wire | Green(G) |
| G | Red wire | Red(R) |
| H | Brown wire | Undefined(null) |

Figure 6.2 Half 9pin cable

If you have any more queries, please contact

Mr. Sambob Wu

Tel/Fax:+86 755-28700114

Cell: +86 135 1046 8916

Email:sam.bob.wu@harmonywolrd.com

Skype: abbula3026

MSN: woll-mart@hotmail.com

# Text boxes

USER’S

MANUAL

| Item | Spec. |
| --- | --- |
| ①MENU | -press it to enter into OSD menu -click it once to select and click again to exit the current line |
| ② “+” | -click it to move the cursor up -click it to add the value |
| ③ “-“ | -click it to move the cursor down -click it to deduct the value |